## Slide 1: VALIDATION
Presented to : Teacher Name
Presented by : Name

## Slide 2: CONTENTS
25 %
        Introduction
        Need of Validation
        Scope of Validation
        Documentation of Validation
        Validation Master Plan
        Types of Validation
        Process Validation
        Cleaning Validation
        Equipment Validation
        Validation of Analytical method
        Conclusion

## Slide 3: INTRODUCTION
        Validation is "Establishing documented evidence that provides a high degree of assurance that a specific process will consistently produce a product meeting its pre-determined specifications and quality attributes.
        This is to maintain and assure a higher degree of quality of food and drug products.
        Customer satisfaction
        Customer mandated

## Slide 4: NEED OF VALIDATION
3
4
1
2
3
4
1
2
THE DEVELOPMENT OF THE NEXT GENERATION
3
PRODUCT LIABILITY
1
CONTROL PRODUCTION COST
2
SAFETY
4

## Slide 5: SCOPE OF VALIDATION
Analytical Test Methods
Process Utility Services
Equipment
Instrument Calibrations
Raw Material
Facilities
Product design
Cleaning
Operators

## Slide 6: DOCUMENTATION OF VALIDATION
The validation activity cannot be completed without proper documentation of each and every minute activity with utmost details.
Documentation of validation is generally different types such as:
Validation Master Plan(VMP)
  Validation Protocol(VP)
      Validation Reports(VR)
  Standard Operating Procedure(SOP)

## Slide 7: TYPES OF VALIDATION
EQUIPMENT VALIDATION
3
PROCESS VALIDATION
1
CLEANING VALIDATION
2
VALIDATION OF ANALYTICAL METHODS
4

## Slide 8: PROCESS VALIDATION
Definition
As per FDA Nov.2008,'The collection of data from the process design stage throughout production, which establishes scientific evidence that a process is capable of consistently delivering quality products.

## Slide 9: TYPES OF PROCESS VALIDATION
3
4
1
2
3
4
1
2
Concurrent Validation
3
Prospective Validation
1
Retrospective Validation
2
Revalidation
4

## Slide 10: CLEANING VALIDATION
Science and Technology, that the cleaning process under consideration does, and
/ or will do, what it purpoes to do.“
Objective..
To minimize cross contamination.
To determine efficiency of cleaning process.
To do troubleshooting in case problem identified in the cleaning process and give suggestions to improve the process.

## Slide 11: EQUIPMENT VALIDATION
Definition
As per FDA, May 1987, 'Action of proving that any equipment works correctly and leads to the expected result is equipment qualification.
It is not a single step activity but instead result from many discrete activities.

## Slide 12: VALIDATION OF ANALYTICAL METHODS
Definition :
“The process by, which it is established, by laboratory studies, that the performance characteristics of the method meet the requirements for the intended analytical application”.

## Slide 13: CALIBRATION
Table of Contents
Definition
Objectives of Calibration
Significance of Calibration
Frequency of Calibration
Calibration Methods

## Slide 14: CALIBRATION
Definition
Calibration is defined as the process of determining the accuracy of an instrument.
This involves:
(a) Obtaining a particular reading from the instrument under study.
(b) Comparing this reading with one obtained from a standard instrument.
(c) Assessing the degree of variation between the two readings.
(d) Adjusting the instrument so that it gives readings in keeping with established standards.

## Slide 15: OBJECTIVES OF CALIBRATION
The calibration of an instrument helps to assess its accuracy. It helps to determine how accurately the instrument is producing results within the prescribed limits.
The main purposes of calibration are:
To ensure instrument/equipment readings display correct readings each time.
To determine how accurate, precise, and reliable are the measurements produced, as well as the degree of deviations that are produced.
To check how reliable the instrument is by examining if it delivers reproducible results.
To assess the degree of drift from accuracy over time.
To ensure adherence to cGMP guidelines for quality.

## Slide 16: SIGNIFICANCE OF CALIBRATION
When instruments and equipment are used regularly, over time, they tend to undergo some of the other damage. This results in a shift in the measurement so that the devices are no longer giving accurate and precise results over the expected range. By measuring the accuracy, precision, and range of such devices, calibration helps to track the shifts and the data generated can be used to rectify the functioning of the instrument.
When calibration is not done for a long time, it may lead to:
Faulty measurements and discrepancies that impact final product quality.
Deterioration of drug materials leading to a safety threat to those consuming the product.
Waste of resources and time.
Loss of time because of the faulty process which has to be shut down and re-started after calibration.

## Slide 17: WHAT IS INSTRUMENT CALIBRATION
Instrument calibration can be defined as the process of comparing the measurements made by the instrument to be calibrated against a known measurement of either standards or an instrument known to be making measurements that exceed the acceptable limits of accuracy and precision.
Usually, calibration labs prefer a standard with 10 times the accuracy; however, most regulating organizations and authorities also accept a 3:1 accuracy ratio.

## Slide 18: FREQUENCY OF INSTRUMENT
The frequency of instrument calibration depends on the nature of its variation or drift from accuracy over time.
It is therefore important to set up a calibration schedule for each instrument such as weekly, monthly, bi-monthly, quarterly, half-yearly, or annually. Generally, instruments need to be calibrated in the following situations:
As soon as it is installed, before it is used for the first time.
Both before and after taking any measurement that is critical to product quality.
When anything out of the ordinary occurs – for example, a fall, bump, or electrical shock is generated.
When readings appear suspect inaccuracy.
After any repair work has been done on the instrument.
As part of a routine calibration schedule.
At all those times recommended by the instrument manufacturer.

## Slide 19: CALIBRATION METHODS
Instruments can be calibrated in several different ways. The method is chosen generally depends on what results in one desire from the calibration exercise and also on particular regulatory requirements like FDA guideline.
Standard Calibration: This method is mostly preferred for calibrating instruments that are non-critical to quality or are not required for accreditation and license purposes: Use traceable standards and document its performance.
Calibration with data: Procedures for calibrations with data are similar to that of accredited calibration. The only exception being that these procedures are not accredited to the ISO standard. Moreover, they are not accompanied by data on measurement uncertainties.
ISO 17025 Accredited Calibration: This has to be the strictest method of calibration. Generally, it requires a measurement report which has the details of the measurements that are made against a standard of 'as found' (before calibration is started) and 'as left (once the calibration is completed). If the calibration is done by a calibration service provider, they must issue a certificate of the same.

## Slide 20: QUALIFICATION
Table of Contents
Definition
Phases of Qualification
WHO Definitions
Considerations While Doing Qualification
Requalification
Factory Acceptance Test and Site Acceptance Test

## Slide 21: QUALIFICATION
Qualification may be defined as the act of proving and documenting that given equipment or process or utility is correctly installed, working properly, and is consistently producing the expected results.
Qualification is a part of the process of validation; however, qualification alone does not complete process validation.

## Slide 22: PHASES OF QUALIFICATION
Design Qualification (DQ)
1
Operational Qualification (OQ)
3
Performance Qualification (PQ)
4
Installation Qualification (IQ)
2

## Slide 23
WHO Definitions
DQ – Documented evidence that the premises, supporting systems, utilities, equipment, and processes have been designed by the requirements of good manufacturing practices.
Design qualification is defined as documented verification that the proposed design of equipment, systems, and facilities is appropriate for the intended purpose. DQ must be performed whenever purchasing new equipment; it should also be performed when existing equipment is going to be used for any new application.
DESIGN QUALIFICATION (DQ)

## Slide 24
WHO Definitions
IQ – The performance of tests to ensure that the installations (such as machines, measuring devices, utilities, and manufacturing areas) used in a manufacturing process are appropriately selected and correctly installed and operate by established specifications.
Installation qualifications defined as documented evidence that the equipment, supporting utilities, and premises have been built or installed in keeping with design specifications. IQ serves to verify that equipment installation has been done as recommended by the manufacturer, correctly, and kept in a suitable environment.
INSTALLATION QUALIFICATION (IQ)

## Slide 25: OPERATIONAL QUALIFICATION
OQ – Documented verification that the system or subsystem performs as intended overall anticipated operating ranges.
Operational Qualification is defined as establishing documented evidence that any equipment, facility, or utility functions as intended, in keeping with its operational specifications. OQ thus helps to verify that the installed equipment works correctly.

## Slide 26: PERFORMANCE QUALIFICATION
PQ – Documented verification that the equipment or system operates consistently and gives reproducibility within defined specifications and parameters for prolonged periods.
Performance Qualification is defined as establishing documented evidence that the process works to consistently produce a product that meets all the predetermined quality requirements. PQ helps to verify that performance within the specified limits is as expected.

## Slide 27: CONSIDERATIONS WHILE DOING QUALIFICATION
Qualification must be performed as per predetermined and approved qualification protocols.
Results must be recorded and should be a part of the qualification reports.
Areas or rooms must be qualified before utilities; utilities must be qualified before equipment.
Equipment can be used only after it has been qualified and documented evidence shows that it is suitable for the intended purpose.
Qualification should be done in a logical sequence – first DQ, then IQ, then OQ, and finally PQ.
All documents related to the qualification process (specifications, standard operating procedures, manuals, acceptance criteria, and certificates) should be maintained.
All equipment, utilities, and systems must be maintained in a qualified state at all times. When necessary, they must undergo periodic requalification.
Validation of processes must be done using qualified equipment only.

## Slide 28: REQUALIFICATION
When any equipment undergoes any kind of modification or relocation on a scale that has a direct impact on the product quality, it must undergo a re-qualification. This process must be handled with a documented change control procedure, after due review and authorization.
Factory Acceptance Test and Site Acceptance Test
In some situations, equipment, or a system or utility may be assembled fully or partially at some other site. In such cases, testing and verification must be performed to ensure it is fit for dispatch, and results must be recorded in the Factory Acceptance Test report before shipment of the item.
After the shipment is received by the end-user, tests must be repeated to verify that the equipment or system, or utility is of acceptable quality. Results of these tests must be recorded in the Site Acceptance Test report.

## Slide 29: THANK YOU